## Slide 1
SEMINAR AT THE CHAIR FOR EMBEDDED SYSTEMS
University of Siegen
Acoustic and Ultrasonic Leak
Detection for Industrial Systems
By Ali Ahmer 1900040
Ali.Ahmer@student.uni-siegen.de
Supervisors Prof. Dr. ing Roman Obermaisser
Utkarsh Raj
Date August 2026

## Slide 2
OVERVIEW
Agenda
01
Introduction
Why industrial leaks matter
02
Fundamental Principles
Acoustic emission & ultrasonic sensing
03
Localization Techniques
TDOA, MED, beamforming, virtual arrays
04
Sensor Technologies
AE sensors, MEMS microphones, Piezoelectric Ultrasonic Sensor
05
Industrial Applications
Pipelines, valves, vessels, plants
06
Machine Learning & Imaging
Classification and acoustic visualization
07
Advantages & Constraints
Benefits and open challenges
08
Future Directions & Conclusion
Where the field is heading
Acoustic & Ultrasonic Leak Detection | University of Siegen
2

## Slide 3
SECTION 1
Introduction
Industrial pipelines and pressure systems carry water, oil, natural gas, hydrogen, steam, and chemicals across large plants and long-distance networks. Corrosion, mechanical stress, fatigue, and accidental damage make leaks a persistent risk.
Why conventional methods fall short
Visual inspection, pressure monitoring, infrared imaging, tracer-gas and mass-spectrometry methods
Slow response times and low sensitivity to small leaks
High operational cost, often requiring a process shutdown to evaluate
[3], [4]
Acoustic & ultrasonic methods enable non-contact, non-destructive, real-time monitoring without disrupting plant operations. [3], [4]
DRIVERS ENABLING MODERN LEAK DETECTION
Signal Processing
Advanced filtering isolates leak signatures from noise
Machine Learning
Automatic classification of leak vs. non-leak signals
Beamforming
Spatial localization of leak sources in real time
MEMS Sensors
Compact, low-cost, highly sensitive microphone arrays
[2], [5], [6]
Acoustic & Ultrasonic Leak Detection | University of Siegen
3

## Slide 4
SECTION 2
Fundamental Principles
Acoustic Emission (AE)
Transient elastic waves released when pressurized fluid escapes through a crack or defect. Turbulent flow, pressure changes, and structural vibration travel through the pipe wall to a sensor.
1
Leak occurs at a crack / opening
2
Turbulent flow generates acoustic waves
3
Waves travel through pipe wall & fluid
4
AE sensors detect the vibrations
5
Signal processing isolates leak features
6
Localization algorithm finds the position
[1], [2], [6]
Ultrasonic Leak Detection (ULD)
Targets frequencies above ~20 kHz. Escaping gas forms high-velocity turbulent jets that emit ultrasonic energy centered around 40 kHz — well separated from industrial background noise.
1
Pressurized gas escapes through a defect
2
Turbulence generates ultrasonic signals
3
MEMS microphone array captures signals
4
Beamforming analyzes spatial data
5
Leak source is identified & visualized
[3], [4], [5]
Acoustic & Ultrasonic Leak Detection | University of Siegen
4

## Slide 5
SECTION 3
Leak Localization Techniques
1
Time Difference of Arrival (TDOA)
<4%
reported localization error
[1], [2] generated by using ChatGPT
2
Minimum Entropy Deconvolution (MED)
Hybrid
MED + dispersion filtering outperforms cross-correlation
[1] generated by using ChatGPT
3
Beamforming Based Acoustic Imaging
Real-time
multi-source imaging
[3] generated by using ChatGPT
4
Virtual Ultrasonic Sensor Arrays
<1°
reported average error
[3] generated by using ChatGPT
Acoustic & Ultrasonic Leak Detection | University of Siegen
5
Arrival-time difference → source position [1]
Sharpens impulsive leak features for first-arrival detection [1]
Align signals across the array → estimate source direction [5]
Scanning positions emulate a larger spatial array [3]

## Slide 6
SECTION 4
Sensor Technologies
Sensor Type
Example
Key Specifications
Ref.
Acoustic Emission Sensor
R15-AST / R15I-AST
50–400 kHz range; resonance at 75 & 150 kHz; ~109 dB peak sensitivity
[1], [2]
MEMS Microphone
SPH0641LU4H-1
~100 Hz–80 kHz range; sensitivity ≈ −38 dBV/Pa; compact & low power
[4], [5]
Piezoelectric Ultrasonic Sensor
FUS-40CR
40 kHz center frequency; 0.2–6 m range; ~50° directivity; ≈ −16 dB sensitivity
[3]
Wireless Acoustic Sensor Node
Remote pipeline nodes
Low power, low maintenance, easy deployment over long networks
[2]
Acoustic & Ultrasonic Leak Detection | University of Siegen
6

## Slide 7
SECTION 5
Industrial Applications & Use Cases
1
Oil & Gas Pipelines
ML-assisted AE systems exceed 99% leak-detection accuracy
[1], [2]
2
Gas Transmission
Strong ultrasonic turbulence signals enable remote leak siting
[3], [4]
3
Internal Valve Leakage
Online inspection without disassembly
[1], [6]
4
Chemical Processing
Remote sensing of hazardous gas leaks & spills for operator safety
[4]
5
Nuclear Facilities
Non-contact inspection in zones hazardous to human access
[4]
6
Pressure Vessels & Tanks
Detects corrosion & fatigue emissions before catastrophic failure
[3], [5]
Acoustic & Ultrasonic Leak Detection | University of Siegen
7

## Slide 8
SECTION 6
The Role of Machine Learning
Recent studies apply machine learning to automatically classify and diagnose leaks — enabling automatic feature extraction, higher classification accuracy, fewer false alarms, and real-time decision-making.
Methods applied in the literature
Artificial Neural Networks (ANN)
Random Forests (RF)
Decision Trees (DT)
K-Nearest Neighbors (KNN)
[1], [2]
REPORTED CLASSIFICATION ACCURACY
99–100%
when acoustic-emission or ultrasonic data are combined with machine-learning classifiers [As reported in literature]
Benefits
• Automatic feature extraction
• Higher classification accuracy
• Fewer false alarms
• Real-time decision-making
[1], [2]
Acoustic & Ultrasonic Leak Detection | University of Siegen
8

## Slide 9
SECTION 7
Advantages
Technical
Real-time monitoring
High localization precision
Sensitive to leaks as low as 24 mL/min at 0.5 m
Remote operation
Early failure identification
[1], [3], [5]
Operational
Non-destructive — no disassembly
No production shutdown needed
Lower maintenance costs
Improved worker safety
Minimal retrofit to existing pipework
[2], [4], [6]
Economical
Reduced product losses
Lower repair costs
Less operational downtime
Extended asset longevity
Improved overall plant efficiency
Acoustic & Ultrasonic Leak Detection | University of Siegen
9

## Slide 10
SECTION 8
Constraints & Challenges
1
Industrial Noise Interference
Motors, compressors, fans and pumps create acoustic interference that complicates signal extraction and can trigger false alarms.
[4], [6]
2
Variable Signal Characteristics
Leak-signal features shift with pressure, temperature, gas type, velocity, geometry and material.
[3], [6]
3
Sensor Placement Sensitivity
Localization accuracy depends heavily on sensor spacing, quantity and array geometry — poor installation sharply reduces accuracy.
[3], [5]
4
Computational Load
Deep-learning methods demand considerable processing resources.
[1], [3], [5]
Acoustic & Ultrasonic Leak Detection | University of Siegen
10

## Slide 11
SECTION 9
Future Research Directions
1
AI / deep-learning leak diagnosis & localization
2
Autonomous inspection robots for hazardous zones
3
Wireless & IoT-enabled sensor networks
4
Digital twins for continuous asset surveillance
5
Enhanced MEMS arrays & beamforming algorithms
6
Multi-sensor data fusion (acoustic + more)
[1], [3], [5], [6]
Acoustic & Ultrasonic Leak Detection | University of Siegen
11

## Slide 12
SECTION 10
Conclusion
Acoustic Emission techniques precisely detect structural flaws and fluid leaks, while ultrasonic methods enable accurate remote identification and visualization of leak origins — supported by advances in signal processing, beamforming, machine learning, and MEMS sensors.
Despite challenges from external noise, nonlinear leak behavior, computational complexity, and limited public datasets, acoustic and ultrasonic techniques remain among the most promising technologies for intelligent industrial monitoring — increasingly powered by AI, IoT, edge computing, and autonomous inspection.
< 1°
Localization error (imaging)
< 4%
Pipeline localization error (TDOA)
> 99%
Classification accuracy
24 mL/min
Smallest detected leak rate
[1], [2], [3], [5]
Acoustic & Ultrasonic Leak Detection | University of Siegen
12

## Slide 13
SOURCES
References
1
Y. Gao, F. Piltan, and J.-M. Kim, "A Hybrid Leak Localization Approach Using Acoustic Emission for Industrial Pipelines," Sensors, vol. 22, no. 10, p. 3963, 2022.
2
N. Ullah, Z. Ahmed, and J.-M. Kim, "Pipeline Leakage Detection Using Acoustic Emission and Machine Learning Algorithms," Sensors, vol. 23, no. 6, p. 3226, 2023.
3
M. Liang, K. Yang, M. Feng, K. Mu, M. Jiao, and L. Li, "Acoustic Imaging Method for Gas Leak Detection and Localization Using Virtual Ultrasonic Sensor Array," Sensors, vol. 24, no. 5, p. 1366, 2024.
4
J. C. Lee, Y. R. Choi, and J. W. Cho, "Pipe Leakage Detection Using Ultrasonic Acoustic Signals," Sensors and Actuators A: Physical, vol. 349, p. 114061, 2023.
5
T. Wang, J. Ji, J. Lan, and B. Wang, "Ultrasonic Beamforming-Based Visual Localisation of Minor and Multiple Gas Leaks Using a MEMS Microphone Array," Sensors, vol. 25, no. 10, p. 3190, 2025.
6
D. Zheng, X. Wang, L. Yang, Y. Li, H. Xia, H. Zhang, and X. Xiang, "Review of Acoustic Emission Detection Technology for Valve Internal Leakage: Mechanisms, Methods, Challenges and Application Prospects," Sensors, vol. 25, no. 14, p. 4487, 2025.
Acoustic & Ultrasonic Leak Detection | University of Siegen
13

## Slide 14
Thank You
Questions & Discussion
Ali Ahmer | Ali.Ahmer@student.uni-siegen.de
Chair for Embedded Systems · University of Siegen